## Slide 2: Bitwise operators

## Slide 3: Topics to cover
Binary representation of numbers
Hexadecimal representation of numbers
Operators
  Not ~
  And &
  OR |
  XOR ^
Shifting Operators
Signed vs Unsigned values

## Slide 4: Binary Numbers
Most of Society operates on a decimal (or Base Ten) number system [0 - 9]
  Meaning, you can represent numbers as a summation of 10N.
  212 = 200 + 10 + 2
  = 2*100 + 1*10 + 2
  = 2*(10*10) + 1*(10) + 2
  = 2*102 + 1*101 + 2*100

## Slide 5: Binary Numbers
You can represent numbers using many different number based systems. Since digital circuits are interested in a high and low state, you can represent numbers using a base 2 (binary) numbering system [0 – 1]
  Summation of 2N numbers
  212 = 128 + 64 + 16 + 4
  = 27 +26 +24+22
  = 1*27+1*26+0*25+1*24+0*23+1*22+0*21+0*20
  → 11010100 (Binary Number)

## Slide 6: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0

## Slide 7: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230

## Slide 8: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230
1115

## Slide 9: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115

## Slide 10: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1

## Slide 11: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557

## Slide 12: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1

## Slide 13: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278

## Slide 14: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0

## Slide 15: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139

## Slide 16: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1

## Slide 17: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69

## Slide 18: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1

## Slide 19: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34

## Slide 20: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0

## Slide 21: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17

## Slide 22: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1

## Slide 23: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8

## Slide 24: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0

## Slide 25: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4

## Slide 26: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4 0

## Slide 27: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4 0
2

## Slide 28: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4 0
2 0

## Slide 29: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4 0
2 0
1

## Slide 30: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4 0
2 0
1 1

## Slide 31: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4 0
2 0
1 1
Least Significant Digit
Most
Significant Digit

## Slide 32: Binary Numbers
Conversion From Decimal to Binary
Divide the number by 2
Get the integer quotient for the next iteration
Get the remainder for the binary digit
Repeat the steps until the quotient is equal to 0
2230 0
1115 1
557 1
278 0
139 1
69 1
34 0
17 1
8 0
4 0
2 0
1 1
Least
Significant Digit
Most
Significant Digit
100010110110

## Slide 33: Binary Numbers
Conversion From Binary to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Multiply digit at index by 2index
Add all the numbers

## Slide 34: Binary Numbers
Conversion From Binary to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Multiply digit at index by 2index
Add all the numbers
100010110110

## Slide 35: Binary Numbers
Conversion From Binary to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Multiply digit at index by 2index
Add all the numbers
100010110110
0
1
2
3
4
5
6
7
8
9
10
11

## Slide 36: Binary Numbers
Conversion From Binary to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Multiply digit at index by 2index
Add all the numbers
100010110110
1*211
0*210
0*29
0*28
1*27
0*26
1*25
1*24
0*23
1*22
1*21
0*20
0
1
2
3
4
5
6
7
8
9
10
11

## Slide 37: Binary Numbers
Conversion From Binary to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Multiply digit at index by 2index
Add all the numbers
100010110110
1*211 = 2048
0*210 = 0
0*29 = 0
0*28 = 0
1*27 = 128
0*26 = 0
1*25 = 32
1*24 = 16
0*23 = 0
1*22 = 4
1*21 = 2
0*20 = 0
0
1
2
3
4
5
6
7
8
9
10
11

## Slide 38: Binary Numbers
Conversion From Binary to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Multiply digit at index by 2index
Add all the numbers
100010110110
1*211 = 2048
0*210 = 0
0*29 = 0
0*28 = 0
1*27 = 128
0*26 = 0
1*25 = 32
1*24 = 16
0*23 = 0
1*22 = 4
1*21 = 2
0*20 = 0
0
1
2
3
4
5
6
7
8
9
10
2048 + 128 + 32 + 16 + 4 + 2 =
11

## Slide 39: Binary Numbers
Conversion From Binary to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Multiply digit at index by 2index
Add all the numbers
100010110110
1*211 = 2048
0*210 = 0
0*29 = 0
0*28 = 0
1*27 = 128
0*26 = 0
1*25 = 32
1*24 = 16
0*23 = 0
1*22 = 4
1*21 = 2
0*20 = 0
0
1
2
3
4
5
6
7
8
9
10
2048 + 128 + 32 + 16 + 4 + 2 =
2230
11

## Slide 40: Hexadecimal Numbers
Sometimes reading a series of 1s and 0s can be confusing, so another format is a popular in Engineering
Can represent numbers as a summation of base 16 [0-F]
  Summation of 16N numbers
  212 = 208 + 4
  = 13*161 + 4*160
  13 → D
  4 → 4
  D4 (Hexadecimal Number)

## Slide 41: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F

## Slide 42: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230

## Slide 43: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230
139

## Slide 44: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230 6
139

## Slide 45: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230 6
139
8

## Slide 46: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230 6
139 11
8

## Slide 47: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230 6
139 11
8
0

## Slide 48: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230 6
139 11
8 8
0

## Slide 49: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230 6 → 6
139 11 → B
8 8 → 8
0

## Slide 50: Hexadecimal Numbers
Conversion From Decimal to Hex
Divide the number by 16
Get the integer quotient for the next iteration
Get the remainder for the hex digit
Repeat the steps until the quotient is equal to 0
Convert values 10-15 to A-F
2230 6 → 6
139 11 → B
8 8 → 8
0
Least
Significant Digit
Most
Significant Digit
8B6

## Slide 51: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers

## Slide 52: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6

## Slide 53: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6
0
1
2

## Slide 54: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6
8
B
6
0
1
2

## Slide 55: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6
8 → 8
B → 11
6 → 6
0
1
2

## Slide 56: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6
8 → 8*162
B → 11*161
6 → 6*16*0
0
1
2

## Slide 57: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6
8 → 8*162 = 2048
B → 11*161 = 176
6 → 6*16*0 = 6
0
1
2

## Slide 58: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6
8 → 8*162 = 2048
B → 11*161 = 176
6 → 6*16*0 = 6
2048 + 176 + 6 =
0
1
2

## Slide 59: Hexadecimal Numbers
Conversion From Hexadecimal to Decimal
Label digits from 0 to N from least significant bit to most significant bit.
Convert Hex digits [A – F] to [10 – 15]
Multiply digit at index by 16index
Add all the numbers
8B6
8 → 8*162 = 2048
B → 11*161 = 176
6 → 6*16*0 = 6
2048 + 176 + 6 =
2230
0
1
2

## Slide 60: Number Conversions
To convert Hexadecimal to Binary (and Vice versa) you can either
  Convert one to decimal and then to the other
  Or use some memorization…
Decimal | Hexadecimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
Decimal | Hexadecimal | Binary
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 61: Number conversion
Using the table, you can group binary bits in groups of 4 and convert them to Hexadecimal numbers
100010110110
6
B
8

## Slide 62: Questions
Given the Decimal number 1234:
Convert to binary

## Slide 63: Questions
Given the Decimal number 1234:
Convert to binary – 10011010010
1234 – 0
617 – 1
308 – 0
154 – 0
77 – 1
38 – 0
19 – 1
9 – 1
4 – 0
2 – 0
1 – 1

## Slide 64: Questions
Given the Decimal number 1234:
Convert to binary
Convert to Hex

## Slide 65: Questions
Given the Decimal number 1234:
Convert to binary
Convert to Hex – 4D2
1234 – 2 → 2
77 – 13 → D
4 – 4 → 4

## Slide 66: Questions
Convert the binary number 1111 1010 1101 to hexadecimal

## Slide 67: Questions
Convert the binary number 1111 1010 1101 to hexadecimal - FAD
1111 – F
1010 – A
1101 – D

## Slide 68: Questions
Convert the hexadecimal number BA5EBA11 to binary

## Slide 69: Questions
Convert the hexadecimal number BA5EBA11 to binary – 1011 1010 011 1110 1011 1010 0001 0001
B – 1011
A – 1010
5 – 0011
E – 1110
B – 1011
A – 1010
1 – 0001
1 – 0001

## Slide 70: Bitwise Operations
In addition to +, -, X, /, and % operations, numbers can also go through operations that affect each bit within the number
Operators
C/C++ operator | Name | Description
~ | NOT | Flips 1s to 0s and 0s to 1s
& | AND | If both bits are 1s, new bit is 1, otherwise 0
¦ | OR | If both bits are 0s, new bit is 0, otherwise 1
^ | XOR | If both bits match, new bit is 0, otherwise 1

## Slide 71: Not Operator
Not operator (~) flips each bit in the number
  1 becomes 0
  0 becomes 1
  Similar to the boolean operator (!)
    True -> False
    False -> True
X = 11 → 1011
~X = ~(11) → 0100 = 4

## Slide 72: And Operator
And operator (&) compares bit by bit between two numbers – both must be 1 to return 1
  Truth Table
  Similar to the boolean operator (&&)
  X = 11 → (1011) X&Y → (1011)
  Y = 7 → (0111) (0111)
  (0011) → 3
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 73: Or Operator
Or operator (|) compares bit by bit between two numbers – either must be 1 to return 1
  Truth Table
  Similar to the boolean operator (||)
  X = 11 → (1011) X|Y → (1011)
  Y = 7 → (0111) (0111)
  (1111) → 15
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 74: XOR Operator
Exclusive Or (or XOR) operator (^) compares bit by bit between two numbers – either must be 1 to return 1, BUT if both are 1, returns 0
  Truth Table
  X = 11 → (1011) X^Y →(1011)
  Y = 7 → (0111) (0111)
  (1100)→ C
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 75: Questions
Given binary numbers
A = 1101 1111 1010 0000 B = 0101 0101 0101 0101
determine
‘A
A&B
A|B
A^B

## Slide 76: Questions
Given binary numbers
A = 1101 1111 1010 0000 B = 0101 0101 0101 0101
determine
‘A = 0010 0000 0101 1111
A&B
A|B
A^B

## Slide 77: Questions
Given binary numbers
A = 1101 1111 1010 0000 B = 0101 0101 0101 0101
determine
‘A = 0010 0000 0101 1111
A&B = 0101 0101 0000 0000
A|B
A^B

## Slide 78: Questions
Given binary numbers
A = 1101 1111 1010 0000 B = 0101 0101 0101 0101
determine
‘A = 0010 0000 0101 1111
A&B = 0101 0101 0000 0000
A|B = 1101 1111 1111 0101
A^B

## Slide 79: Questions
Given binary numbers
A = 1101 1111 1010 0000 B = 0101 0101 0101 0101
determine
‘A = 0010 0000 0101 1111
A&B = 0101 0101 0000 0000
A|B = 1101 1111 1111 0101
A^B = 1000 1010 1111 0101

## Slide 80: Bit Shift Operators
<< and >> mean something different in C and C++
  C++ - Insertion (<<) and Extraction (>>)
  C – Shift Left (<<) and Shift Right (>>)
Shifting operators take 2 arguments
  X << n or X >> n
  X is the variable for shifting
  n is by how many bits to shift either way

## Slide 81: Bit Shift Operators
<< Example
X = 50 → 0011 0010
Y = X<<2 → 1100 1000 → Y = 200
>> Example
X = 20 → 0001 0100
Y = X >>2 → 0000 0101 → Y = 5
NOTE: A shift to the left or right by N position is equivalent to multiplying or dividing an integer by 2N

## Slide 82: Bit Shift Operators
Issues
  Overflowing: For unsigned integers, the 1 has the possibility of shifting outside of the scope of the integer. That 1 is gone and has overflowed
    X = 12 → 1100 X<<1 = 1000 → 8
    X = 3 → 0011 X>>1 = 0001 → 1
  Shifting does not change the value in of itself. Shifting must be assinged

## Slide 83: Bitwise operators
Assignment operators – a way assign a change to a variable
Operator | Symbol | Form | Operation
Left Shift Assignment | <<= | X<<=Y | Shifts X left by Y bits
Right Shift Assignment | >>= | X>>=Y | Shifts Y right by Y bits
Bitwise Or Assignment | ¦= | X¦=Y | Assigns X¦Y to X
Bitwise And Assignment | &= | X&=Y | Assigns X&Y to X
Bitwise Xor Assignment | ^= | X^=Y | Assigns X^Y to X

## Slide 84: Questions
Given X = 55 (unsigned integer) with a maximum number of bits of 8.
  What is the result of X <<=2
  What is the result of X >>=2

## Slide 85: Questions
Given X = 55 (unsigned integer) with a maximum number of bits of 8.
  What is the result of X <<=2
  X = 0011 0111
  X<<2 = 1101 1100 → 220
  What is the result of X >>=2

## Slide 86: Questions
Given X = 55 (unsigned integer) with a maximum number of bits of 8.
  What is the result of X <<=2
  X = 0011 0111
  X<<2 = 1101 1100 → 220
  What is the result of X >>=2
  X = 0011 0111
  X >> 2 = 0000 1101 → 13

## Slide 87: Questions
Given X = 55 (unsigned integer) and Y = 88 (unsigned integer) with a maximum number of bits of 8 for each .
  What is the result of X &=Y
  What is the result of Y ^=(~X)

## Slide 88: Questions
Given X = 55 (unsigned integer) and Y = 88 (unsigned integer) with a maximum number of bits of 8 for each .
  What is the result of X &=Y
  X = 0011 0111
  Y = 0101 1000 → X&Y = 0001 0000 = 16
  What is the result of Y ^=(~X)

## Slide 89: Questions
Given X = 55 (unsigned integer) and Y = 88 (unsigned integer) with a maximum number of bits of 8 for each .
  What is the result of X &=Y
  X = 0011 0111
  Y = 0101 1000 → X&Y = 0001 0000 = 16
  What is the result of Y ^=(~X)
  X = 0011 0111 → ~X = 1100 1000
  Y = 0101 1000 → Y^(~X) = 0001 0000 = 0

## Slide 90: Negative Numbers in Binary
So far, we have only talked about how to represent positive integers with binary numbers, but negative integers can also be represented if we sacrifice one bit to represent the positive or negative sign
Traditionally, the Most Significant Bit has been used for sign
  0 – Positive number
  1 – Negative Number

## Slide 91: Negative Numbers in Binary
Sign Magnitude Representation – make MSB to 1
+12 with 8 bits 0000 1100
-12 with 8 bits 1000 1100
Issues with Sign Magnitude Represenation
  Doing arithmetic operations can be challenging
  Incrementing +12 → +13 0000 1100 → 0000 1101 (+13) 
  Incrementing -12 → -11 1000 1100 → 1000 1101 (-13) 

## Slide 92: Negative Numbers in Binary
One’s complement Representation – take the inverse of the positive number
+12 with 8 bits 0000 1100
-12 with 8 bits 1111 0011
Issues with One’s Complement Representation -Two representations of zero
  +0 with 8 bits 0000 0000
  -0 with 8 bits 1111 1111

## Slide 93: Negative Numbers in Binary
Two’s complement Representation – take the inverse of the positive number and increment by one
+12 with 8 bits 0000 1100
-12 with 8 bits (1’s) 1111 0011
-12 with 8 bits (2’s) 1111 0100
Why? It makes addition and subtraction a little easier in binary

## Slide 94: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101

## Slide 95: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
1

## Slide 96: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
01

## Slide 97: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
001
1

## Slide 98: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
0001
1

## Slide 99: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
1 0001

## Slide 100: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
01 0001

## Slide 101: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
001 0001

## Slide 102: Negative Numbers in Binary
Binary Addition
Decimal: 12 + 5 = 17
Binary: 0000 1100
+ 0000 0101
0001 0001

## Slide 103: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)

## Slide 104: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
1

## Slide 105: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
11

## Slide 106: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
111

## Slide 107: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
0111
1

## Slide 108: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
0 0111
1

## Slide 109: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
00 0111
1

## Slide 110: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
000 0111
1

## Slide 111: Negative Numbers in Binary
Binary Subtraction
Decimal: 12 - 5 = 12 + (-5) = 7
Binary: 0000 1100
+ 1111 1011 (2’s complement)
0000 0111
1 - overflow

## Slide 112: Questions
Represent -23 in
  Sign Magnitude Representation
  One’s Complement Representation
  Two’s Complement Representation

## Slide 113: Questions
Represent -23 in
  Sign Magnitude Representation
  23 – 0001 0111
  -23– 1001 0111
  One’s Complement Representation
  Two’s Complement Representation

## Slide 114: Questions
Represent -23 in
  Sign Magnitude Representation
  One’s Complement Representation
  23 – 0001 0111
  -23– 1110 1000
  Two’s Complement Representation

## Slide 115: Questions
Represent -23 in
  Sign Magnitude Representation
  One’s Complement Representation
  Two’s Complement Representation
  23 – 0001 0111
  -23 – 1110 1001

## Slide 116: Questions
Represent Given X as 23 and Y as 15,
  Calculate X+Y
  Calculate X-Y

## Slide 117: Questions
Represent Given X as 23 and Y as 15,
  Calculate X+Y
  X = 0001 0111
  Y = 0000 1111
  X+Y = 0010 0110
  Calculate X-Y

## Slide 118: Questions
Represent Given X as 23 and Y as 15,
  Calculate X+Y
  Calculate X-Y
  X = 0001 0111
  Y = 0000 1111
  -Y = 1111 0001
  X+Y = 0000 1000